Build Crypto++ dynamically on Microsoft Windows and Visual C++

1. Grab a copy of the latest source release of Crypto++ and extract it somewhere.

2. Open up cryptest.sln in VC++ IDE

3. There are 4 projects in the solution, and the only one that we need to build shared version of Crypto++ is the crypopp project. So, right click on the cryptopp project and ensure that you have the following settings for the project in both Debug and Release build modes:

Note: Default project file for building the dynamic version which ships with Crypto++ uses static linking (/MT or /MTd). This is so wrong, and it should be /MD or /MDd. Despite the fact that dynamic version builds just fine, you will end up in plenty of ambiguous linker errors when linking your own code against the dynamic version of Crypto++. The reason is that your are linking against different versions of the run-time libraries. So, do not mix static and dynamic versions of the run-time libraries.

Note: Due to errors in shared-lib builds, rename the debug files manually and add _d postfix to their names. Also, for both release and debug rename VC80.pdb to cryotopp.pdb and cryptopp_d.pdb for each build acoordingly.

Debug:
    Configuration Properties > C/C++ > Code Generation > Runtime Library > Multi-threaded Debug DLL (/MDd)

Release:
    Configuration Properties > C/C++ > Code Generation > Runtime Library > Multi-threaded DLL (/MD)

4. Now build the cryptopp project in both Debug and Release build modes. If everything goes smoothly, grab these files and copy them to your lib folder:

Debug:
    {Crypto++ Source Directory}\Win32\DLL_Output\Debug\cryptlib_d.lib
    {Crypto++ Source Directory}\Win32\DLL_Output\Debug\cryptlib_d.pdb

Release:
    {Crypto++ Source Directory}\Win32\DLL_Output\Release\cryptlib.lib
    {Crypto++ Source Directory}\Win32\DLL_Output\Release\cryptlib.pdb

5. Last but not least, copy all the *.h files from the extracted Crypto++ source directory to {your own include directory}/cryptopp.